## Slide 1
ARTIFICIAL INTELLIGENCE
AI-Based Color Sensor
Combining optoelectronic sensing with machine learning to classify color intelligently
PRESENTED BY
P Dinesh Reddy
192525399
GUIDED BY
Dr M Prakash

## Slide 2
What Is an AI-Based Color Sensor?
An AI-based color sensor pairs an optoelectronic sensor — which measures the wavelength of light reflected from an object — with a machine learning model that classifies the reading. Instead of relying on fixed thresholds, the model learns decision boundaries from labeled examples, turning a raw RGB or spectral value into a class, label, or grade.
QUICK FACTS
380–700 nm
Visible light wavelength range detected
3–4 channels
Typical RGB / RGBC sensing channels
90–98%
Typical classification accuracy once trained
< 5 ms
Typical response time of modern sensors
02

## Slide 3
System Architecture
How data flows from raw light to a classified output
HARDWARE LAYER
Light
Source
→
RGB Filter
Array
→
Photodiode
Array
→
ADC / Signal
Processor
↓
digitized RGB / spectral reading
AI / SOFTWARE LAYER
Feature
Vector
RGB / spectral values arranged as model input
→
Trained ML
Model
Learned decision boundaries classify the reading
→
Classification
Output
Color class, quality grade, or automated action
03

## Slide 4
Training the Color Classifier
From labeled reflectance data to a deployed classification model
Data Collection
& Labeling
Hundreds of RGB readings are captured per color class under varied lighting, then labeled to build a training dataset.
e.g. 200+ samples/class
Feature Extraction
& Model Choice
Readings are normalized into RGB ratios or HSV features, then fed to a classifier such as k-NN, SVM, or a shallow neural network.
e.g. k-NN, SVM, ANN
Training &
Evaluation
The dataset is split into training and test sets; accuracy, precision, and a confusion matrix show how well the model generalizes.
e.g. 95%+ test accuracy
04

## Slide 5
Applications
Where AI-driven color
sensing shows up in the real world
Industrial Sorting
A trained classifier sorts fruit, plastics, and parts by color on production lines.
Robotics & Line Following
Color-based features help a robot's model follow lines and markers autonomously.
Print & Packaging QC
Anomaly-detection models flag color deviations and registration errors automatically.
Cosmetics & Skin Tone
ML models match foundation shades and analyze skin tone from sensor readings.
Agriculture
A classifier assesses fruit ripeness and crop quality from color and spectral data.
Display Calibration
A regression model closes the loop to keep screen color output calibrated.
05

## Slide 6
Advantages & Limitations
ADVANTAGES
– Compact, low-cost, and easy to integrate with microcontrollers
– Fast enough for real-time inference in sorting and robotics
– No moving parts, making it durable and low-maintenance
– Learns subtle color boundaries that are hard to code manually
LIMITATIONS
– Sensitive to ambient lighting and shadows unless shielded
– Model accuracy depends on the quality and coverage of training data
– Requires calibration and labeled examples before deployment
– Short sensing distance compared to camera-based systems
06

## Slide 7
SUMMARY
Conclusion
Color sensors turn something as ordinary as reflected light into precise, actionable data — filtering it into RGB or spectral bands and converting it to a digital signal a trained model can classify and act on. Paired with AI, that simple principle now underpins intelligent sorting lines, robots, print inspection, cosmetics matching, agriculture, and display calibration.
Thank you